## Slide 1: Design of Adaptive Motor Controller with Built in Microcontroller and I2C Control
Senior Design Project
Justin Derickson

## Slide 2: Objective
The objective of this project is to develop a standalone system that will address power distribution, motor and servo control, and general input and output in a single unit.
Notes: Asked by a colleague to help troubleshoot some wiring issues with a research project.
Diagrams were not kept up to date.
Electronics enclosure was crowded and disorganized.
Total disassembly was required to fix issue.

## Slide 3: Design Requirements
Hardware and Firmware requirements
Three sets of requirements:
Output Requirements
Power and Control Requirements
System should be small and inexpensive.

## Slide 4: Design Requirements: Input andOutput
Control a single bipolar stepper motor or up to two DC motors
5 - 24V operating voltage
1.5 A maximum current per winding or motor
general purpose I/O for quadrature encoder feedback
PWM output for stepper motor control

## Slide 5: Design Requirements: Power and Control
power supply voltage from 9 - 24 V
provide a stable 5V source to power external devices
I2C and PWM compatible
General I/O
Notes: I2C would like come from a raspberry pi or arduino.
PWM would likely come from an RC receiver.
PWM more likely to control lower level functions like throttle and steering.
I2C and onboard switches will dictate higher functions

## Slide 6: Design Constraint
Budget

## Slide 7: System Diagram
System Diagram:

## Slide 8: System Functions
Motor Driver:
Accept logical input for bipolar stepper motor control.
Allow for DC motor control using came connections as stepper motor.
Microprocessor
Supplies control logic to motor driver.
Communicates with external devices.

## Slide 9: Task List
Task 1. Control System Design
Task 2. Power System Design
Task 3. Verification
Task 4. PCB Design
Task 6 Final Assembly and Testing

## Slide 10: Implementation of Tasks
Circuit Design Week 1 - Week 10
Prototyping / Testing Week 11 - Week 13
PCB Layout Week 14 - Week 17
Firmware Coding Week 18 - Week 21
Assembly and Testing Week 22 - Week 24
Projected Timeline and Delivery Plan over 45 weeks

## Slide 11: Task 1 Control Section Design

## Slide 12: Task 1: CircuitMaker by Altium
Free
Large, community-driven component database
Components linked to footprints and vendors
3D-Rendering capability

## Slide 13
Finalized Schematic

## Slide 14: Task 1: Control Section Design Motor Driver Requirements
Implement Full, Half, and Microstepping in a Bipolar Stepper Motor.
    Independent dual DC motor control.

## Slide 15
Task 1: Control Section Design Motor Driver
H-Bridge
Change direction of current through load.
Change current through load with Enable

## Slide 16: Task 1: Control Section Design Motor Driver: L298N
L298N Dual H-Bridge
  Max Supply Voltage 48V
  Logic Supply Voltage 5V
  Total DC current 4A
  Enable pin for each winding
  Current Sensing

## Slide 17: Task 1: Control Section Design Motor Driver: Schematic
D1 – D8 are 2A fast switching diodes to protect against back emf from motors

## Slide 18: Task 1: Control Section Design Microcontroller: Requirements
I2C and PWM for device and sensor interfacing.
UART for USB Programming.

## Slide 19: Task 1: Control Section Design Microcontroller: ATmega328PB
  Operating Voltage: 1.8 to 5.5V
  Memory: 32KB
  Programmable Flash: 1KB EEPROM 2KB SRAM
CPU speed: 20 MIPS @ 20MHz
  PWM Peripherals: 10 channels
  Communication Peripherals: 2-UART, 2-SPI, 2-I2C

## Slide 20: Task 1: Control Section Design Motor Driver: Schematic

## Slide 21: Task 2 Power Section Design 5V Supply
LM340MP Linear Regulator
Operating Voltage 7.5V - 35V
Output voltage 5V
Output Current 1A
Notes: Current Calculations

## Slide 22: Task 2: Power Section Design
Two Separately controllable voltage regulators
Controlled by a single I2C dual channel digital potentiometer

## Slide 23: Task 2 Power Section Design Variable Supply Schematic
C9 improves transient response.
C8 improves ripple rejection.
D9 & D10 provide discharge path around regulator.
Notes: C9 improves transient response. C8 improves ripple rejection. D9 & D10 provide discharge path around regulator output.

## Slide 24
LM338 Adjustable Linear Regulator
Operating Voltage: 4.2V - 40V
Output voltage 1.24V – 32V
Output Current 5A
Task 2 Power Section Design Variable Supply
Schematic

## Slide 25: Task 2 Power Section Design: Digital Pot
AD5248BRMZ10
I2C compatible
2-Channel, 256 position potentiometer
10kΩ end to end resistance
Single supply 2.7v to 5.5v
Notes: While this component is designed as a LED driver, It produces a PWM output easily configured for operating servos.

## Slide 26: Task 3 Programming/ Debugging Design: AVR-ISP connector
  AVR Devices are initially programmed through a 6 or 10 pin header connected to pins on the microcontroller
  This device will use a 6 pin header
  Needed to install bootloader that runs programs and allows for serial programming through usb e.g. Arduino
  Single wire debugging is done through reset pin of isp header

## Slide 27: Task 4 : System Verification

## Slide 28: Task 4 Design Verification the ATmega328PB Xplained development board
Inexpensive: $9.00 on Amazon
DebugWire: Debugging through ISP port using serial communication on RESET pin
Arduino Compatible: Arduino header connectors can be added to board for debugging using arduino.

## Slide 29: Task 4 Design Verification L298N Motor Driver Board Modifications
Replaced Power, Input, and Enable connectors with breadboard compatible header pins
Cut Sense Pins from board to connect 0.5  current sense resistors.

## Slide 30: Task 4 Design Verification Digital Potentiometer Breakout Assembly

## Slide 31: Task 4 Design Verification Completed Test Assembly
Notes: Connect bottom ground and add 10k pull up resistor

## Slide 32: Task 4 Programming/Debugging: Sparkfun Pocket AVR Programmer
  Inexpensive
  Can program all microcontrollers supported by AVRDUDE
  Works with microcontrollers with 64KB or less memory
  Also supports single wire debugging

## Slide 33: Task 4 Design Verification: IDE Selection
Free
Compatible with multiple AVR programmers
Software Simulation for most AVR microcontrollers
Atmel Studio

## Slide 34
Simulated Stimuli on Atmel Studio

## Slide 35: Task 4: Control Section Design Microcontroller: PWM
A modulation technique that encodes information into the width of a regular pulse.
Current control can be achieved by varying the amount of time that a device is on.

## Slide 36: Task 4
ATmega328PB Block Diagram

## Slide 37
Vary input logic for different combinations of forward, back, and stop
Use PWM to vary power to each motor individually
Task 1: Design Verification Motor Control
Dual DC Motor Operation

## Slide 38: Task 4

## Slide 39: Task 4: Design Verification Motor Control Full, Half, and MicroStepping
  Full and Half stepping relies on input logic.
Microstepping varies power to each winding in varying proportion.
  PWM to vary power by duty cycle

## Slide 40: Task 4

## Slide 41
    Serial communication protocol transfers information one bit at a time.
Addressed devices are connected to same line
Devices respond when they see their address after the start condition.
Task 1 Control Section Design Microcontroller: I2C

## Slide 42: Task 4

## Slide 43: Task 5 : PCB Design

## Slide 44: Task PCB Design OSHPARK design rules
$5 per square inch
Order in Multiples of three

## Slide 45: Task PCB Design PCB layout guidelines
Keep Trace Lengths Short
Power and Ground Planes
Group Related Components Together

## Slide 46: Task PCB Design Recommended Circuit Layouts

## Slide 47: Task PCB Design Via and Trace Calculation

## Slide 48
Finalized PCB in Circuit Maker

## Slide 49
Finalized PCB in Circuit Maker

## Slide 50: Task PCB Design Bill Of Materials Production
Part Selection In Schematic Design
Octopart BOM Tool
Total Part Cost

## Slide 51
OSHpark Production Render

## Slide 52: Questions?